## Slide 1: 8086 - Flag, Minimum Maximum Mode

## Slide 2
Md. Shoayeb Hossain
MEET OUR GROUP
Mr. Mozdaher Abdul Quader
Dept of CSE
Green university of Bangladesh.
Md. Al Mamud
222002106
222002105
Mim Akter
222002104

## Slide 3: Table of contents 01 02 03 04
Flag Register
Minimum Mode
Details about 8086 Minimum mod pin.
Details about 8086 flag register pin.
Conclusion
Conclued about our presentation.
Maximum Mode
Details about 8086 Maximum mod pin.

## Slide 4: Flags

## Slide 5: Sign Flag (S) 02 04 01 Zero Flag (Z) Auxiliary Carry Flag (AC) 03 Parity Flag (P) Carry Flag (CY) 05 Overflow Flag (O) 06 Status Flag
MSB indicate the sign bit.
Indicates a carry between bits 3 and 4 during mathematics operations.
Tells us whether or not our answer has been zeroed.
In the result of an arithmetic or logical operation is even or odd.
Shows whether there was a carry on the(MSB) during mathematics operations.
This bit is raised when the result of a signed operation goes beyond limits of the data type.

## Slide 6: Control Flags Direction Flag (DF) Interrupt Flag (IF) Trap Flag (TF) Flags
Decides on the direction of string operations, it can vary from forwards to backwards.
That can turn ON or OFF maskable interrupts.
If DF=1, the string instruction will automatically decrement the pointer. If DF=0,the string instruction will automatically increment the pointer.
If TF=1, the CPU automatically generates an internal interrupt after each instruction, allowing a program to be inspected as it executes instruction by instruction.
If IF=1, the CPU will recognize external interrupt request (Interrupt Disabled). If IF=0, then interrupt disabled.
May help in debugging one instruction at a time by turning on single step mode.

## Slide 7: Minimum Mode 02

## Slide 8: Minimum Mode
Overview
Operates when MN/MX’ = 1.
Only processor in the system which provides all the control signals.
The circuit is simple but it does not support multiprocessing.
Transceivers, latches, 8284 clock generator, 74138 decoder, memory and i/o device.
The address bus of 8086 is 20 bits long.

## Slide 9: Minimum Mode
Circuit
Control signals provided by 8086 for memory operations and i/o interfacing :
They are used to identifying whether the bus is carrying a valid address or not , in which direction data is needed to be transferred over the bus, when there is valid write data on the data bus and when to put read data on the system bus.

## Slide 10: Minimum Mode
8286 (8 bits) transceivers
They are bidirectional buffers and also known as data amplifiers.

## Slide 11: Minimum Mode
Timing diagram
The working of min mode can be easily understood by timing diagrams.

## Slide 12: — Maximum Mode — 03

## Slide 14
The transceivers are enabled the DEN signal.
The direction of data is controlled by the DT/R signal.
DEN is connected to OE' and DT/R' is connected to T. Both DEN and DT/ R' are given by 8288 bus controller.
— Maximum Mode —

## Slide 15: — Real-World Examples —
Minimum Mode
Home appliances, calculators.
Maximum Mode
Cloud servers, data centers.

## Slide 16: — Comparison of Minimum and Maximum Modes —
Feature | Feature | Feature
Configuration | Single-processor | Multiprocessor
MN/MX# Pin Setting | Logic '1' | Logic ‘0'
Control Signals | Internal | External

## Slide 17: — Conclusion —
The 8086’s Minimum and Maximum Modes demonstrate its versatility, allowing it to adapt to a wide range of system requirements. Understanding these modes is essential for designing efficient computing systems.

## Slide 18: Thanks!
Do you have any questions?